## Slide 2: Contents
Management
  Philosophy
  Management Roadmap
Company Overview
  History
  Products Introduction
  Manufacturing Process Overview
  Annual Production Capacity
  Sales Figure
Global Operation
  Korea (HQ / Daegu)
  Vietnam (Ho Chi Minh)

## Slide 3: Management

## Slide 4
Philosophy
Value Creation
“Beyond Customers’ Satisfaction”

## Slide 5: Management Roadmap
Vision
Top Class Global Driveline Parts Manufacturer
Policy
Customer’s Happiness is Our Success
Goal (by 2021)
  Quality : “0 ppm” customer quality
  Cost : Lowest cost competitiveness
  Revenue : 20M USD

## Slide 6: Management Roadmap
Mission
  Operation : Top class quality and productivity
  System : Exceed IATF16949 requirements
  Marketing : Long term partnership with Global Player
Strategy
  HR : Interdependent key functional staff by experts
  Management system : Quarterly review and upgrade
  Value stream : Integration of Up-stream and Down-stream
  Communication : Focus on Team Consensus build
  Marketing : Pursuit for exclusive partnership with target customer
  Global footprint : Customer centers and/or Representative offices
  Sourcing : Quality focus

## Slide 7: Company Overview

## Slide 8: History
May. | 2022 | IATF16949 Certified(Vietnam)
Mar. | 2019 | Sunghoon-Vietnam Established
Mar. | 2018 | IATF16949 Certified
Jan. | 2018 | HQ Relocation to New Plant
Nov. | 2017 | Start of Production (CVJ Inner Races & Cages)
Sep. | 2007 | TS16949 Certified
Mar. | 2007 | Start of Production (Tripot Spider Assemblies)
Sep. | 2005 | Sunghoon-China Established (Dalian / Compressor Heads)
Jul. | 2003 | ISO9000 Certified
Jan. | 2001 | Start of Production (CVJ OR & TJ Housing Machining)
Oct. | 2000 | Technical License of Grinder Technology (Meccanodora / Italy)
Apr. | 1994 | Sunghoon Corp. Established (Manufacture of M&E, Automation)
Apr. | 1992 | Sunghoon International Established (Trading of Machineries)

## Slide 9: Overview of Products

## Slide 10: Products (Driveline)
Tripot Spider Assembly
  Standard
Premium
  Tri-Glide (Nexteer)
    27size : GM (Cruz)
    34size : GM (Lacross)
  KPJ (erae-AMS)
    19size : Kubota
    26size : GM (Bolt), SYMC (Korando)
    32size : FCA (C200)
    34size : FCA (Pacifica)
    37size : FCA (RAM)

## Slide 11: Products (Driveline)
Ball Joint Cages
  Rzeppa
    6-ball standard (erae-AMS)
      34size : FCA (Pacifica)
      37size : FCA (RAM)
    6-ball HA (erae-AMS)
    6-ball HE (erae-AMS)
  CGJ
    6-ball standard (Dae-Seung)
      21size : HMC (Santa-Fe)
  DOJ
    6-ball standard (erae-AMS)
      26size : FCA (C200)
      40size : FCA (Pacifica)

## Slide 12: Products (Driveline)
Ball Joint Inner Races
  Rzeppa
    6-ball standard (erae-AMS)
      34size : FCA (Pacifica)
      37size : FCA (RAM)
    6-ball HA (erae-AMS)
    6-ball HE (erae-AMS)
  CGJ
    6-ball standard (Dae-Seung)
      21size : HMC (Santa-Fe)
  DOJ
    6-ball standard (erae-AMS)
      26size : FCA (C200)
      40size : FCA (Pacifica)

## Slide 13: Manufacturing Process Overview
Tripot Spider (Korea / HQ)
＃10 Processing I.D and Face / ＃20 Broaching
＃60 Blast/Surface Texture
＃50 Ultrasonic Washing
＃40 Trunnion Grinding
＃30 Carburize, Quench & Temper
Material Inflow(F.W)
Heat Treater (Outsource)
＃80 Eddy Current ＆ Marking
＃70 Ultrasonic Washing
Moving to stock Area
(Driveline)

## Slide 14: Manufacturing Process Overview
Outer Roller (Korea / HQ)
＃10 Pro | cessing O.D and Face,＃20 Proces | sing
of I.D and Face |  | 
＃60 Washing
＃50 O.D Grinding , # I.D Grinding
＃40 Double Disc Grinding
＃30 Carburize, Quench & Temper
Material Inflow(F.W )
＃90 Class Marking
＃80 Polishing
＃100 Eddy Current Test
Moving to Assembly line
Heat Treater (Outsource)
(Driveline)

## Slide 15: Manufacturing Process Overview
Roller (Korea / HQ)
＃ | 10 Processing O.D and Face,＃20 | 
Processing of I.D and Face |  | 
＃60 Ultrasonic Washing
＃50 O.D Grinding, ＃60 I.D Grinding
＃40 Double Disc Grinding
Material Inflow(F.W )
＃90 Eddy Current Test
＃80 Polishing
Moving to assembly line
＃30 Carburize, Quench & Temper
Heat Treater (Outsource)
(Driveline)

## Slide 16: Manufacturing Process Overview
Roller & Spider Assembly (Korea / HQ)
＃20 Dispense Needles to
Outer Roller
＃60 100% Visual Check
＃50 Press Fit 3-Roller Asm.
to Spider
＃40 Vision Check Number
of Needles
＃10 Identify Outer Roller
Class
＃30 Match Inner Roller
＃70 Packing
(Driveline)

## Slide 17: Manufacturing Process Overview
Cage (Korea / HQ)
(Driveline)
Tube
Cutting
Forming
Turning
OD/ID
Punching OR
Fine Blanking windows
Broaching OR
Soft milling windows
Carburizing
Grinding OD/ID
Grinding OR
Hard milling windows
Polishing

## Slide 18: Manufacturing Process Overview
Inner Race (Korea / HQ)
(Driveline)
Turning
OD/ID
Broaching Internal Spline
Carburizing
Grinding
OD
Grinding
Tracks

## Slide 19: Sales Figure

## Slide 20: Company Overview

## Slide 21: History
Nov. | 2018 | ‘HAJIN VINA HIGH TECH “ Established (Land area to be used : 12,213㎡) Objectives of the project: Manufacturing of and process out and Inner races,cage,spider and in,out ball
Jan. | 2019 | 1st Investment Capital($800,000)
Sep. | 2019 | 2st Investment Capital($800,000)
Nov. | 2019 | Factory buiiding completed(Total Floor Erea: 7,437.24㎡)
Mar. | 2020 | 3st Investment Capital($800,000)
Apr. | 2021 | 4st Investment Capital($528,222.7)
Apr. | 2022 | 5st Investment Capital($1,000,000) (Total Investment Capital: $3,928,222.7)

## Slide 22: Overview of Products
Key Parts & Characteristics
Part | Outlook | Characteristic | Tolerance | Remarks
INLET-RH (11.54.936.729.027) |  | Inner Diameter | Φ130.60±0.2 | 1Kinds
 |  | Outer Diameter | Φ97.5±0.3 | †
 |  | Position | Φ0.5 | †
 |  | Roughness | Ra 3.2 | †
INLET-LH (11.54.936.729.028) |  | Inner Diameter | Φ130.60±0.2 | †
 |  | Outer Diameter | Φ97.5±0.3 | †
 |  | Position | Φ0.5 | †
 |  | Roughness | Ra 3.2 | †
(VIỆT NAM / VN)

## Slide 23: Manufacturing Process Overview
INLET-RH (11.54.936.729.027)
＃20 MCT M/C
＃30 CNC M/C
Material Inflow(F.W)
＃10 MCT M/C
＃40 Leaktest, Rust oil
#50 Storage & Packaging

## Slide 24: Manufacturing Process Overview
INLET-LH (11.54.936.729.028)
＃20 MCT M/C
＃30 CNC M/C
Material Inflow(F.W)
＃10 MCT M/C
＃40 Leaktest, Rust oil
#50 Storage & Packaging

## Slide 25: Manufacturing Process Overview
INLET-RH (11.54.936.729.027)
Material Inflow(F.W)
＃10 MCT M/C
＃20 MCT M/C
＃30 CNC M/C
＃40 Leaktest,
Rust oil
#50 Storage & Packaging
INLET-RL (11.54.936.729.028)

## Slide 26: Sales Figure
Chart: 
| Tháng 6 | Tháng 9 | Tháng 10 | Tháng 11 | Tháng 1 | Tháng 2 | Tháng 3 | Tháng 4 | 2021 | 2022
SCM | 333001659 | 1237420600 | 1333476300 | 480711400 | 590764200 | 929532500 | 995285200 | 1069932725
SỐ LƯỢNG GIA CÔNG | 12282 | 25726 | 27723 | 9994 | 12688 | 11008 | 28296 | 22737

## Slide 27: Global Operation Korea (HQ / Daegu) Vietnam (Ho Chi Minh)

## Slide 28: Korea Operation (HQ / Daegu)

## Slide 29: Organization
Affiliates
HAJIN : Trading & Auto Parts in Vietnam
SUNG-A Tech. : Domestic Sales
CEO
Auto Parts
M/C & Tool
Trading
Administration
CVJ Parts
Grinders
Special Purpose M/C
Grinders
MCT
V-Lathe
Build
(Korea / HQ)

## Slide 30: Plant Layout (Korea / HQ)
.
Roller Turning
Spider Turning & Broach
O/R & I/R Soft Milling
Spider Asm.
After Grind for Ball
Spider & Ball Grinding
Cage & I/R Grinding
Material Stock
Material Stock
Material Stock

## Slide 31: Manufacturing Facilities (Korea / HQ)
Equipment | Maker | Country | Quantity | Remark
External Grinder | Sunghoon | Korea | 17 | Spider : 5, Inner Race : 1 Cage :5, Ball: 6
Internal Grinder | Sunghoon | Korea | 12 | Ball: 8 cage :4
Double disc Grinder | Shinhan | Korea | 1 | 
Centerless Grinder | Hanhwa | Korea | 1 | 
(6)Windows Grinder | Meccanodora | Italy | 2 | Cage
Assembly Machine | Sunghoon | Korea | 6 | Spider ASM
Washing M/C | ilsung | Korea | 2 | 
Polishing M/C | Roesler | Germany | 1 | 
Shot Blast M/C | Roesler | Germany | 1 | 
Buffing M/C | Hyundai-wia | Korea | 4 | 
Window Punching Press | Georg | Germany | 1 | Cage
Window Broaching M/C | Varinelli | Italy, Korea | 1 | Cage
IR Track Grinder | Sunghoon | Korea | 3 | Inner Race
Lathe | Hyundai-wia | Korea | 30 | 
OR/IR Track Milling M/C | Sunghoon | Korea | 1 | 
 | Meccanodora | Italy | 1 | 
Broaching m/c | KMT | Korea | 1 | 
Windows hard /soft mill | Sunghoon | Korea | 1 | Cage

## Slide 32: Manufacturing Facilities (Korea / HQ)
Equipment | Maker | Country | Quantity | Remark
Polishing(Barrel) M/C | Rosler | Germany | 1 | 
Forming Press | Shandong ludi industry | China | 1 | Cage
Cutting M/C | Sunghoon | Korea | 1 | Cage

## Slide 33: Quality Inspection Facilities (Korea / HQ)
Equipment | Maker | Country of Manufacturer | Specifications | Year | Remark
Con-tracer | Tokyo-Seimitsu | Japan | 1700SD | 2007 | 
Roundness Tester | Tokoyoseimitsu | Japan | Randcom 44SD | 2007 | 
Roughness Tester | Tokoyoseimitsu | Japan | Surfcom 480A | 2007 | 
Vickers Hardness Tester | Mitsutoyo | Japan | HM | 2007 | 
Profile Projector | Mitsutoyo | Japan | 172-847D | 2012 | 
CMM | Carl-Zeiss | Germany | Contura G2 776 AKTIV | 2013 | 
Rockwell Hardness Testing M/C | KIM Tech | Korea | DTR-200N | 2013 | 

## Slide 34: Quality Inspection Facilities (Korea / HQ)
Con-tracer
Roundness
Tester
Roughness
Tester
Hardness Tester
Carl Zeiss CMM
Profile Projector

## Slide 35: QMS (Korea / HQ)
Real Time SPC Monitoring System

## Slide 36: QMS (Korea / HQ)
Key Parts & Characteristics
Part | Outlook | Characteristic | Tolerance | Remarks
Spider |  | Trunnion O.D | ±0.013 | 34T/31T 2Kinds
 |  | BCD | ±0.03 | †
 |  | Position | Φ0.1 | †
 |  | Position | Φ0.2 | †
Outer Roller |  | Outer Diameter | ±0.007 | †
 |  | Outer Dia. C/L | ±0.05 | †
 |  | Inner Diameter | ±0.007 | †
Inner Roller |  | Outer Diameter | ±0.007 | †
 |  | Inner Diameter | ±0.007 | †
 |  | Inner Dia. C/L | ±0.05 | †

## Slide 37: Vietnam Operation (Ho Chi Minh)

## Slide 38: Organization
(VIỆT NAM / VN)

## Slide 39: Plant Layout
(Vietnam)
대지 : 12,213㎡ 건평 : 8,890㎡
Potential

## Slide 40: Manufacturing Facilities (VIỆT NAM / VN)
Equipment | Maker | Country | Quantity | PART
CNC LATHE | WIA | Korea | 4 | CAGE
Cage internal Grinder | Sunghoon | Korea | 1 | CAGE
Cage external grinder M/C | Sunghoon | Korea | 1 | CAGE
Cage Window Milling | Sunghoon | Korea | 1 | CAGE
Cage Window Punch Press |  | Japan | 1 | CAGE
CNC LATHE | WIA | Korea | 6 | INNER RACE
Broach M/C | KM | Korea | 1 | INNER RACE
External grinder | Sunghoon | Korea | 1 | INNER RACE
Inner Race Track Grinding M/C | Sunghoon | Korea | 1 | INNER RACE
CNC LATHE | WIA | Korea | 1 | SPIDER
Trunnion grinding M/C | Sunghoon | Korea | 1 | SPIDER
CNC LATHE | WIA | Korea | 1 | FLANGE
CNC LATHE | WIA | Korea | 1 | FLANGE
Machining Center F500MV | WIA | Korea | 1 | FLANGE
Machining Center F500D | WIA | Korea | 4 | FLANGE

## Slide 41: Manufacturing Facilities (VIỆT NAM / VN)
Equipment | Maker | Country | Quantity | PART
Vertical Machining Center F410D | WIA | Korea | 3 | FLANGE
Machining Center NTT 70D | Komatec | Korea | 2 | FLANGE
Mazak MCT | Mazak | China | 5 | FLANGE
BCF | Dong Woo | KOREA | 2 | HEAT TREATMENT
Washing machine 01 Bottom Plate | Dong Woo | KOREA | 1 | HEAT TREATMENT
Temparing Furance | Dong Woo | KOREA | 1 | HEAT TREATMENT
Endothermic Gas Generator | Dong Woo | KOREA | 1 | HEAT TREATMENT
Shot Blast M/C | Ding Tai | China | 2 | HEAT TREATMENT
Nitriding Furnace | SOO IN |  | 2 | HEAT TREATMENT (MOULD)
Machining Center F660M | WIA | Korea | 2 | MOULD

## Slide 42: Quality Inspection Facilities (VIỆT NAM / VN)
Equipment | Maker | Country of Manufacturer | Specifications | Year | Remark
Coordinate Measuring M/C | Mitutoyo | Japan | BH-V507 |  | 
Roundness Measuring M/C | Tokoyoseimitsu | Japan | Randcom 44SD |  | 
Contour Measuring M/C | Mitutoyo | Japan | CV-200 |  | 
Sueface Measuring M/C | Tokoyoseimitsu | Japan | Surfcom-480A |  | 
Inverted metallurgical microscope | Nikon | Japan | MA-100N |  | 
Micro Vickers Hardness Teser | Mitutoyo | Japan | HAR-M-31 |  | 
Polisher M/C | Hanalum Eng. | Korea | HAR-P-250 |  | 
Profile Projector | Mitsutoyo | Japan | 172-847D |  | 
Cutting M/C |  | Korea |  |  | 
Rockwell Hardness Testing M/C | KIM Tech | Korea | DTR-200N |  | 
Mounting M/C | Hanalum Eng. | Korea |  |  | 

## Slide 43: Quality Inspection Facilities (VIỆT NAM / VN)
Con-tracer
Roundness
Tester
Roughness
Tester
Hardness Tester
Mitsutoyo CMM
Inverted metallurgical microscope

## Slide 44: “Customer’s Happiness Is Our Success”
Thank you for attention!